## Slide 1: Chapter 5
Custom Configurations

## Slide 2: Need for custom Configurations
You might be given a list of requirements from a client and need to translate that into the optimal system for their needs

## Slide 3: A+ Exam
On the A+ exam, you may be given a scenario and asked to choose the
right PC configuration to meet customer needs. Each of the next eight
sections on different configurations gives you the information needed to
choose the right configuration based on a given scenario. For example, if
given a scenario where the user will be designing magazines, he or she will
need a graphic or CAD/CAM workstation. Or, if the user wants to store all
of the family’s important files in a central location, they might consider a
home server PC.

## Slide 4: Specialized Systems
Standard thick clients
Graphic and CAD/CAM design workstations
Audio/video editing workstations
Virtualization workstations
Gaming PCs
Home theater PCs
Thin clients
Home server PCs
Notes: core components don’t differ dramatically in functionality from one type of system to the next. For example, a hard drive is designed to store files; this doesn’t change

## Slide 5: 1. Standard Thick Clients
A thick client is a standard client computer system
It’s the standard configuration on which custom configurations are based.
This is the type of client that users need unless they are performing specialized duties requiring extra hardware or software.
Minimum OS requirements, standard applications such as MS Office
Minimum RAM, HDD space, Network capabilities can’t be assumed
Notes: Each operating system requires a minimum set of hardware features to support its installation – RAM, CPU, HDD Space etc.
Keep in mind that minimum specifications are just that, the minimum. Better performance is realized by using recommended specifications or higher.

## Slide 6: 2. Graphic and CAD/CAM Workstations
Designers of graphical content, such as posters, advertisements, magazines, product packaging, and other graphic media
Engineers or architects
Need:
CPU enhancements
Video Enhancements
Maximized RAM…..

## Slide 7: i. CPU Enhancements
Graphic design workstations are used by desktop publishers in the creation of high-quality copy consisting of professional text and graphical images. This output is used in advertising, marketing, and other forms of specialized documentation.
CAD/CAM workstations are used in the design of engineering and architectural documentation, including blueprints in both two and three dimensions.
Notes: Similar yet distinct functions

## Slide 8
The best type of CPU for these types of systems will often be a multicore processor
Each core can execute instructions independently, which greatly speeds up the system’s performance
Quad Core processor at minimum
Notes: When selecting a multicore processor, the amount of cache is also a very
important consideration. Each core should have a sufficient amount of L1
and L2 cache dedicated to it, and L3 cache will be shared among them. A
16-core processor with 40MB of cache will greatly outperform a 16-core
processor with only a 16MB cache.

## Slide 9: ii. Video Enhancements
Best technology within budget is required by Graphic design and CAD/CAM Workstations
Video adapters with better graphics processing units (GPUs) and additional RAM on board have the capability to keep up with the demand of graphic design applications.

## Slide 10: iii. Maximized RAM
Maximizing the amount of RAM that can be accessed by the CPU and operating system will result in better overall performance by graphic design workstations.
PS - Before upgrading your RAM, always check to see what type of RAM is compatible with the motherboard, how many slots are available, and how the slots work together.
Notes: Graphics applications tend to be particularly CPU and RAM hungry
They process numerous instructions via CPU and RAM holds these numerous instructions

## Slide 11: 2. Audio/Video Editing Workstations
Require:
Video enhancements
Specialized audio
Specialized hard drives

## Slide 12: i. Video Enhancements
Audio/video editing workstations benefit most from a graphics adapter with multiple video interfaces that can be used simultaneously
Dual Monitor is a must – for multiple viewing of same or similar files
Also required is a high resolution monitor
Notes: Extended desktop - In video editing, many packages optimize their desktop arrangement when multiple monitors are detected, allowing less horizontal scrolling through timelines.
CUDA (Compute Unified Device Architecture) and OPENCL (Open Computer Language)
To improve video-editing performance, insist on a graphics adapter that supports CUDA and OpenCL. CUDA is NVIDIA’s Compute Unified Device Architecture, a parallel computing architecture for breaking down larger processing tasks into smaller tasks and processing them simultaneously on a GPU. Open Computing Language (OpenCL) is a similar, yet cross-platform, open standard. CUDA is for NVIDIA drivers only.

## Slide 13: ii. Specialized Audio
Editors of audio information who are expected to perform quality work often require six to eight channels of audio and not the standard 2 channels in standard cards
In addition to audio output, many A/V editors will require the ability to input custom music from an electronic musical keyboard or other device. A term you will hear in relation to this is the musical instrument digital interface (MIDI) standard
Notes: 5.1 or 7.1 Audio cards are available but Digital audio cards preferred

## Slide 14: iii. Specialized Hard Drives
Use separate drives for System and Data files
Use large and fast Data drives for faster encoding and processing
SATA 6Gbps spinning at 7200RPM or faster are recommended
SSD cards can be considered but have a size, cost limitation
Notes: They use Non-Linear Editing Software (NLE) – i.e allow you to access any part of the frame (audio or video) and can cut and paste. NLE software example is Adobe Premier
When using a hard drive get one with an eSATA port – Sata is internal while eSATA is external
Also Thunderbolt and USB3 drives are recommended
RAID 0 drives (stripped) provide faster read and write (simultaneous). Simple volumes can store larger files like RAID 0 but not write simultaneously and therefore slow.
For fault tolerance get RAID 5 which also has RAID 0 speeds
PS: Redundancy duplicates equipment keeping one active while the other idle. Fault tolerance both are active and if one fails the other kicks in

## Slide 15: 3. Virtualization Workstations
Virtualization in detail is discussed in Ch. 20
It allows for multiple guest OSs to run on the same computer at the same time, along with a host OS.
Each virtual machine (VM) running on a host system appears to come along with its own resources

## Slide 16: Virtualization workstations
The following components are shared by the host and all guest OSs:
CPU Cycles
System Memory
Drive Storage
System-wide Network Bandwidth
Therefore CPU Enhancements (multicore) and Maximized RAM must exceed standard workstations
Notes: Many CPUs or CPU cores are recommended because they are shared
A multicore CPU can use cores to work on specific VMs - Dedicated core
As you create a virtual machine, even before a guest operating system is installed in the VM, you must decide how much RAM the guest system will require.
The RAM is only used when the VM is booted, therefore the combined RAM must take into consideration how many VMs you plan to install

## Slide 17: Virtualization Workstation
The following 3 constraints determine how much RAM can be installed:
CPU address-bus width
Operating System Maximum supported RAM
Motherboard’s Maximum supported RAM

## Slide 18: 4. Gaming PC’s
Today’s advanced PC-based gaming software cannot be expected to run on an average system.
Specialized gaming computers are optimized for running modern video games
PC Gaming is a growing segment of the personal-computer market.

## Slide 19: Gaming PC enhancement areas
4 areas of enhancement must be considered:
CPU enhancements
Video enhancements
Specialized audio
Enhanced cooling

## Slide 20: i.CPU Enhancements
CPU must be able to create the action
Mid-level to high end multicore will suffice
Gamers overclock the CPU to reach clock speeds greater than the manufacturer by making changes in the bios to the clocking frequency to dominate competitors
Overclocked CPUs don’t last long though

## Slide 21: ii.Video Enhancements
Technologies like NVIDIA’s SLI and ATI’s Crossfire are extremely beneficial for such graphics-intensive applications.
Video cards for gaming systems essentially require their own dedicated graphics processing unit (GPU)
The choice of monitor must keep up with the speed of the adapter, its resolution or 3D capabilities
Notes: Gamers can now get 12GB or 16GB RAM on their video cards

## Slide 22: iii. Specialized Audio
High definition digital audio from technologies such as S/PDIF and HDMI are required
Headsets with Microphones

## Slide 23: iv. Enhanced Cooling
As mentioned overclocked CPUs used by some gamers don’t last long due to heat output
High end graphics cards come with their own cooling fans
Gaming-PC builder’s decision to include two or more ganged adapters (video cards that are two expansion slots wide and take up two expansion slots but attached together as one unit) in one system (SLI or Crossfire) challenges the engineered cooling circuit.

## Slide 24: 5. Home Theater PCs
Today though, home theater PCs (HTPCs) are becoming more popular as specialized computing appliances used to control the entire home entertainment experience.
They store large amounts of video media streamed out to display devices, stream from the internet or act as A/V tuners and receivers
HTPCs give users more control over their set-top boxes

## Slide 25: HTPCs continued
The following list comprises the specializations inherent in true HTPCs:
Video enhancements
Specialized audio
Special chassis
TV tuner requirement

## Slide 26: i. Video enhancements
High Definition Multimedia Interface (HDMI) offer high def. audio and high def. video and therefore a logical choice
Graphic adapters with one of more HDMI interfaces
Monitor should be state of the art too

## Slide 27: ii. Specialized audio
HDMI is capable of 8-channel 7.1 surround sound ideal for home theater
High end digital audio should be near the top end of the wish list
Minimum should be 7.1 analog surround sound (six 3.5mm stereo mini jacks)
PS: stereo mini jacks are the ones you find on a standard headphone set

## Slide 28: iii. Special chassis / iv. TV Tuner
HTPCs have their own specialized computer case form factor (case design)
These should blend well with other home appliances such as DVRs, DVD players etc
Typically black, sit horizontal like desktop computers and have touch screen interfaces

## Slide 29: HTPC features..
Typical dimension 17”x17”x7
Motherboard typically mini-ITX with integrated HDMI
Blu-ray drive, PCIe or USB TV Tuner card, HDD or SSD (large storage)
RAM for mini-ITX, SODIMMs for prebuilt models

## Slide 30: 6. Thin Clients
A thin client is any machine that divests itself of all or most local storage and varying levels of RAM and processing power without necessarily giving up all ability to process instructions and data.
It resembles but is not a dumb terminal (which only displays output to the monitor and relays input from keyboard and mouse to the server)
Thin clients feature a true network connection but have low processing power and storage, meaning the server must have increased capacities. This unfortunately leads to one central point of failure

## Slide 31: Thin Clients continued..
Their Operating Systems can be simple and designed specifically for thin clients
For example Thinstation, Windows Embedded Standard (WE7) and Lenovo Terminal Operating System (LeTOS)
Thin clients can feature flash-based storage and small form factor RAM which distinguish them from Thick clients

## Slide 32: 7. Home Server PCs
Home server PCs are essentially powerful client systems with a standard, non-server OS.
These have many features of a server but don’t necessarily have server Operating System and are thus capable of allowing other clients to have limited access, but not enough access to accommodate a large number of users.

## Slide 33: Home Server PCs continued..
Fault tolerance should be considered.
PS: Fault tolerance seeks to retain accessibility during the failure while redundancy simply ensures recoverability after the failure.
For example having run-flat tires allows you to continue to drive even when a puncture occurs (Fault Tolerance). Redundancy means having more of what you need for example a spare tire in case you get a flat

## Slide 34: Home Server PC enhancement features:
Media streaming capabilities
File sharing services
Print sharing services
Gigabit NIC
RAID array

## Slide 35: i. Media streaming capabilities
Home server PCs stream music, photos, and videos to other devices including those that are not PCs.
Windows 7 and newer allow media streaming services
In Windows 7, Microsoft introduced HomeGroups (password protected) similar to WorkGroups but with a smaller scope and security requirements
HomeGroups can share files and devices such as printers
Exercise 5.1 shows how to enable media streaming

## Slide 36: ii. File and Print sharing
Streaming occurs in one direction from the server and does not affect the client’s file system.
But file sharing can go in both directions, and it adds to the client’s file system during downloads.
The server acts as a repository for uploaded files that can then be downloaded from any other machine in the home network.
Difference between Enterprise servers and Home servers is that all systems in the home have equal access to files and printers while enterprise servers have permission level access to the data store that allow or restrict access to users
Notes: Static, one directional

## Slide 37: iii. Gigabit NIC
Home server should be hard wired to a switch or wireless access point
The NIC (Network Interface Card) should be capable of Gigabit speeds
Running client NICs at gigabit speeds should be avoided, even though the capability is ubiquitous.
Running all devices on the network at gigabit speeds guarantees that each device that is attached will attempt to saturate the server’s gigabit interface with its own traffic.

## Slide 38: iv. RAID Array
Because some of the data stored on a home server represents the only copy, it must be protected from accidental loss
Large storage capacity is desirable
Fault tolerance is advised
Hardware RAID relieves the server from managing the array
It should include hot-swappable drives so that it can be rebuilt on the fly while still servicing client requests during the loss of a single drive.

## Slide 39: Custom Configuration Enhancements Summary
Graphics, CAD/CAM | A/V editing | Virtualization | Gaming PCs | Home Theater PCs | Thin Clients | Home Server PCs
CPU enhancements | Specialized Audio | CPU enhancements | CPU enhancements | Specialized Audio | ** | Media Streaming Capabilities
Video Enhancements | Video Enhancements | Maximized RAM | Video Enhancements | Video Enhancements |  | File and Print sharing services
Maximized RAM | Specialized HDD |  | Specialized Audio | Special Chasis |  | Gigabit NIC
 |  |  | Enhanced Cooling | TV Tuner |  | RAID Array